## Slide 1: STUN: Secret-Free Trust-Establishment For Underground Wireless Networks
Ebuka Oguchi, Nirnimesh Ghose, Mehmet C. Vuran
School of Computing
SIXTH WORKSHOP ON 5G & BEYOND WIRELESS SECURITY , IEEE INFOCOM 2022
May 2 – 5, 2022

## Slide 2: Background
Agricultural Internet of Things (Ag-IoT):
  Increased Productivity in farm yields
  Wireless Enabled smart farming
  Soil monitoring, Plant health, smart irrigation, etc.
Fig 1: Ag-IoT

## Slide 3: Motivation
Safer automated farming practices to prevent various threats like active signal injection attacks.
Secured transmission and Reception of wireless sensor data.
Data collected by the sensors can be secured by initial trust establishment.
Initial trust establishment includes authentication and secure key establishment between underground sensor and over the air gateway .

## Slide 4: Objectives
To develop a secret free trust establishment for underground wireless communication.
  Secure key establishment by performing Message Integrity verification using hard to forge wireless properties.
  Authentication between the trusted node and gateway node
  We show that the security of STUN is comparable to unbalance oil and Vinegar public key cryptographic scheme.
Adversary (M)
Legitimate Nodes
Trusted Node
Gateway

## Slide 5: Threat Model
Type 1 Adversary
Type 2 Adversary
Type 1 adversary which attempts to inject its signals simultaneously at G and T
Adversary is outside the perimeter of the farm.
Type 2 adversary can deploy additional nodes above and underground to achieve the receive signal strength (RSS) at G and T

## Slide 6: STUN: Trust Establishment Protocol
G
L
T
Initialization
Sync Message
Sync Message
Compute and transmit
Compute and transmit
Records RSS (1), …, (l)}
Verification Criterion:
(k)
Transmit
G Records RSS for L (1), …, (l)} also for T, (1), …, ()}
Decrypt and compares
Verification Criterion:
(k)
Compute and transmit
Key establishment: Receives message computes pairwise key
Key establishment:
G computes pairwise key

## Slide 7: STUN: Received signal strength Verification
Verification at T (step 3):
Verification at G(step 5):

## Slide 8: Evaluation: Type 1 Adversary
Condition for adversary to defeat type 1 adversary:
Equal transmit powers in step 3 and 5 to pass the verification at the distance,
simulataneously.
Secondly, = 1.

## Slide 9: Evaluation: Type 2 Adversary
Adversary above ground may be able to compute for step 5 since the channel is visible.
To compute underground. It has to compute a system of equations.
The solution to this system of S multivariant quadratic equation is known to be NP-hard (UOV public cyptosystem).
  Minimum number of legitimate node per trusted node is 4

## Slide 10: Experimental Setup
We utilize a 433 MHz Underground testbed[3],[4] with 30% VWC.
Testbed utilizes antenna with 30-69cm
G uses Full-Wave dipole antenna
L and T uses Single Ended Elliptical antenna with 10dB gains
Distances = 0.35m, = 0.40m, = 7.8m,
Power transmit =10mW, 37 bytes packet size, 100ms inter packet time and TinyOS app to implement message transmission between nodes.
[3] X. Dong, M. C. Vuran, and S. Irmak, “Autonomous precision agriculture through integration of wireless underground sensor networks with center pivot irrigation systems,” Ad Hoc Networks, vol. 11, no. 7, pp. 1975– 1987, 2013
[4] A. R. Silva and M. C. Vuran, “Empirical evaluation of wireless underground-to-underground communication in wireless underground sensor networks,” in Proc. of International Conference on Distributed Computing in Sensor Systems. Springer, 2009, pp. 231–244.

## Slide 11: Experimental Evaluation: Type 1 Adversary
Fig 8: Plot of distance and power transmitted against distance between T and G.
M must be place extremely far from G
Step 3 fails
  High attenuation.
  Adversary needs to transmit very high power
  L trasmit on 3W
Very high
distance
Very high
Power

## Slide 12: Experimental Evaluation: Type 2 Adversary
Fig 9:success probability of type 2 adversary against distance between M and T
We choose powers between [1- 10W] randomly,
Threshold, = 2.512 to = 6.309
We ran experiment 10,000 times on testbed .
The success probability, and (very low probability)
Very low Success probability
Very low Success probability

## Slide 13: Conclusion and Future Work
We address the problem of a secret free secure bootstrap for COTS underground nodes with an aboveground gateway.
We used hard to forge underground wireless propagation laws to achieve in band node authentication and secret establishment.
We proved that STUN has security equivalent to UOV scheme in cryptography.
In the future, we plan to experimentally evaluate and optimize the placement of trusted nodes to cover an agricultural farm and also develop security for G-to-L communication link.
Q&A